## Slide 1: Swerve Drive
RatPack 830

## Slide 2: Goals
Everyone understands the fundamentals of swerve software
Everyone learns and codes in c++
Robust, reliable swerve software implementation
Reusable splining solution for use in Auto

## Slide 3: Timeline
July 23rd – Swerve Driving well in Teleop
August 6th – Swerve Odometry Working
  Important for splining
August 27th – Splining Working

## Slide 4: Swerve Components
Swerve Module
Gyro
Absolute Encoder
Turn Motor
Drive Motor

## Slide 5: Swerve Module
Turn Motor
Set wheel to a specific heading
Infinite rotation
Position PID
Drive Motor
Drive wheel at a specific speed
Velocity PID

## Slide 6: Others
Module Absolute Encoder
Provide a way to set the zero heading regardless of where the modules are facing
Gyro
Used for field centric drive
  Forward is always towards opposite alliance wall
Provides a heading bounded from 0-360 deg

## Slide 7: C++ Interface
Describes functions that a class must implement
Example:
Advantage: programming to interface allows others to develop without needing an actual class implementing the functionality
Advantage: if we change one physical component, we just need to implement a new class for it and don’t have to rewrite entire swerve

## Slide 8: SwerveGyro
GetYawPitchRoll()
GetHeading()
GetRawHeading()
Get/SetInverted(bool inverted)
SetZeroHeading(double zero_heading)

## Slide 9: SwerveAbsoluteEncoder
GetHeading()
GetRawHeading()
Get/ SetInverted(bool inverted)
SetZeroHeading(double zero_heading)

## Slide 10: SwerveTurnMotor
SetRotation(double deg)
GetRotation()
Get/ SetInverted(bool invert)
ForceTurnDirectionCW()
ForceTurnDirectionCCW()
SetIdleMode()
GetIdleMode()

## Slide 11: SwerveDriveMotor
SetVelocity(double desired_vel)
GetVelocity()
Get/ SetInverted(bool inverted)
SetIdleMode()
GetIdleMode()

## Slide 12: SwerveModule
SetState(SwerveModuleState state)
GetState()
SetIdleModes()
GetIdleModes()

## Slide 13: SwerveDrive
Get/SetEbreak()
Drive(Translation2d pos, double rotation)
Drive(double vx, double vy, double omega)
Drive(ChassisSpeeds speed)
Drive(SwerveModuleState[] states)
Set/Get Idle Modes
SetRobotOriented()
SetFieldOriented()

## Slide 14
Sendable wpilib – look into this
Create overall interface with DumpData() to output to dashboard